oVirt SR-IOV support
Alona Kaplan
Senior Software Engineer
Red Hat
16/09/15

---
Agenda
- SR-IOV basics.
- oVirt Networking basics.
- oVirt Implementation of SR-IOV.
- Future improvements.

---
What is SR-IOV?
specification that allows a PCIe device to appear to be multiple separate physical PCIe devices.

---
Physical Function (PF)
Full PCIe device that includes the SR-IOV capabilities.

---
Virtual Functions (VFs)
’lightweight’ PCIe functions that contain the resources necessary for data movement but have a carefully minimized set of configuration resources.
[Speaker Notes: Cost effective Max Vfs Changing num of vfs (all the exisiting vfs are removed and new ones are created)]

---
Example- how to add VFs
Before
Add VFs
After

---
Using VFs
- As regular nics.
- Directly attaching to a VM.

---
Advantages of attaching VF to a VM
- VFs have near-native performance.
- low latency.
- scalability of the host is improved (more CPU available to apps in VMs).
- VM has direct access to the hardware.
- data protection between guests.
- VMs can share a single physical port.

---
Infrastructure

---
Limitations
- VFs number is limited by the device hardware.
- Realistic 'num of VFs' should be set manually.
- VFs have limited configuration functions.
- Complexity in live migration.

---
Requirements
- hypervisor
  - hardware IOMMU support (AMD-Vi, Intel VT-d enabled in BIOS) .
  - kernel enabled IOMMU support (intel_iommu=on for Intel, amd_iommu=on for AMD in kernel cmdline) .
  - SR-IOV capable hardware.
  - RHEL7 or newer (kernel >= 3.6).
- SR-IOV support in the guest driver.
[Speaker Notes: Using qemu-img Libguestfs]

---
oVirt Networking
- Logical Network (VM, non-VM).
- Setup networks.
- VM Interface (vNic).
- VM Interface Profile (vNic profile).

---
Logical Network

---
Host Networks setup

---
Connecting vNic to a Network

---
oVirt Implementation of SR-IOV
- Passthrough vNic profile.
- Passthrough vNic.
- Host nic VFs configuration-
  - Networks white list.
  - Number of VFs.

---
Passthrough VM Interface profile

---
Passthrough VM Interface

---
Setup Networks

---
VFs configuration

---
oVirt SR-IOV capabilities
- Managing PFs network connectivity white-list.
- Scheduling – no need to pin to a host.
- Setting VLAN and MAC address on a VF.
- Change & persist number of VFs (sysfs) via ui/rest.
[Speaker Notes: Validate space on storage domain Storage domain path + mount]

---
SR-IOV capabilities- cont
- Mixed mode- bridged PF with VFs.
- Specifying boot order on VFs (enabling booting VM with passthrough vNics from pxe).

---
oVirt SR-IOV future capabilities
- Hot plug/unplug passthrough vnics.
- Pin vNic to spepecific VF.
- 'Nice to have' passthrough vNic.
- Live migration.

---
Missing functionality
- MTU
- QoS (in/out- average link share, upper limit, real time).

---
Harware issues
- VFs share the IOMMU group.
- IOMMU is not supported (the devices doesn’t get iommu-group number).
- Hacks are needed
  - pci=realloc - ‘igb <0000:02:00.1>: not enough MMIO resources for SR-IOV’
  - pci=assign-busses - ‘igb <0000:06:10.0>: SR-IOV: bus number out of range’
  - vfio_iommu_type1.allow_unsafe_interrupts=1: broken interrupt remapping.

---
THANK YOU!
http://www.ovirt.org
alkaplan@redhat.com
alkaplan@irc.oftc.net#ovirt